## Slide 1
Workshop
Best practices (Best Practice How to present measures)
This project has received funding from the European Union’s H2020 Coordination Support Action under Grant Agreement No.785047.
Towards a Sustainable Agro-Food Industry. Capacity Building Programmes in Energy Efficiency.

## Slide 2
Initial Situation: 5.000 MWh
  Electricity per year: 5.000 MWh
  Electricity Price: 200 €/MWh
  Natural Gas per year: 3.500 MWh
  Natural Gas Price: 50 €/MWh
Efficiency Measure (Heat Regeneration, High Efficiency Pumps,…)
  Investment: 230.000 €
  Electricity Consumtion after Measure 4.945 MWh
  Gas Consumtion after Measure 2.485 MWh
  Technical live cycle: 10 years
  Cost Savings per year: 61.750 €
We developed a measure for the Washing Plant
Fuente: CCO open picture
Example: Optimisation of a cycle washing plant

## Slide 3
Chart: 
| End of year 1 | End of year 2 | End of year 3 | End of year 4 | End of year 5 | End of year 6 | End of year 7 | End of year 8 | End of year 9 | End of year 10
Cumulated Savings | -168250 | -106500 | -44750 | 17000 | 78750 | 140500 | 202250 | 264000 | 325750 | 387500
Savings | 61750 | 61750 | 61750 | 61750 | 61750 | 61750 | 61750 | 61750 | 61750 | 61750
85% of the companies only evaluate Savings on behalf of pay back time
Source: Fraunhofer ISI
Pay-back Calculation

## Slide 4
But the measure is really good!
Wait, we show you the detailed technical evaluations
Leave me alone with those technical details, I want an Investment Calculation
Source: CCO open picture
Source: CCO open picture
Not advisable to argue with technical details
Better speak their language
Example: Optimisation of a cycle washing plant.

## Slide 5
Present Valor:
Value at the present moment of a summary sum in the future, calculated the application to it of a discount rate that the interest rates and the risk element of the transaction are retracted.
Total Present Value = Present Value of Cash Flows (Savings) – Investment = 325.000 euros
Return on Investment (als percentage) = Total Present Value / Investment = 141%
Total Present Value of an Investment
Chart: 
| Investment | End of year 1 | End of year 2 | End of year 3 | End of year 4 | End of year 5 | End of year 6 | End of year 7 | End of year 8 | End of year 9 | End of year 10
Total Present Value | 324674.6241
Present Value | 554674.6241
Investment | -230000
Cash Flow | 61750 | 61750 | 61750 | 61750 | 61750 | 61750 | 61750 | 61750 | 61750 | 61750

## Slide 6
Chart: 
| Investment | End of year 1 | End of year 2 | End of year 3 | End of year 4 | End of year 5 | End of year 6 | End of year 7 | End of year 8 | End of year 9 | End of year 10
Total Present Value | 324674.6241
Present Value | 554674.6241
Investment | -230000
Cash Flow | 61750 | 61750 | 61750 | 61750 | 61750 | 61750 | 61750 | 61750 | 61750 | 61750
Deducted by calculatory yield: 2% p.a.
Valor presente total de una inversión
Present Valor:
Value at the present moment of a summary sum in the future, calculated the application to it of a discount rate that the interest rates and the risk element of the transaction are retracted.
Total Present Value = Present Value of Cash Flows (Savings) – Investment = 325.000 euros
Return on Investment (als percentage) = Total Present Value / Investment = 141%

## Slide 7
Chart: 
| Investment | End of year 1 | End of year 2 | End of year 3 | End of year 4 | End of year 5 | End of year 6 | End of year 7 | End of year 8 | End of year 9 | End of year 10
Total Present Value | 324674.6241
Present Value | 554674.6241
Investment | -230000
Cash Flow | 61750 | 61750 | 61750 | 61750 | 61750 | 61750 | 61750 | 61750 | 61750 | 61750
24% p.a.
Internal Rate of Revenue: comparable with a “repayment credit”.
Yield, where Investment - Total Present Value
Valor presente total de una inversión

## Slide 8
The Cash Flows over 10 y. are worth 325.000 € today, even considering 2% inflation
You would need an investment of 24% yield p. a. to be equally profitable.
But this machine is standard equipment and we will use it for over 10 years for sure.
Why not get a credit from the bank for 2% p. a. interest rate?
Arguing like this is easy: with the INDUCE profitability calculator
Source: CCO open picture
Example: Optimisation of a cycle washing plant

## Slide 9
Ejemplo: Optimización de una planta de ciclo de lavado.

## Slide 10
Example: Optimisation of a cycle washing plant.

## Slide 11
Towards a sustainable agro-food industry. Capacity building programmes in energy efficiency.