## Slide 1
Concept and Introduction of the Energetic efficiency in the company
This project has received funding from the European Union’s H2020 Coordination Support Action under Grant Agreement No.785047.
Towards a Sustainable Agro-Food Industry. Capacity Building Programmes in Energy Efficiency.

## Slide 2
3.3.EN.2_Concept and Introduction of the Energetic efficiency in the company
Version of: 3.3.EN_Introduction of the Energetic Efficiency in the company.
Description of the changes: Add some first slides where the concept of energy efficiency and the consequences of energy consumption are explained.
List of resources used: 3.2.EN_Awareness in Energy Efficiency.

## Slide 3: Energy Efficiency
¿What is?
Steeep: Support & training for an Escellent Energy Efficiency Performance
Energy efficiency focuses on technology, equipment or machinery used in buildings.
Energy saving is based on the way
people act to use less energy (for
example, using natural light
instead of artificial light to
reduce electricity consumption).
technologies that require a smaller
amount of energy to achieve the
same performance or perform the
same function
It refers to the use of

## Slide 4
¿Why it is important?
Energy Efficiency
Source: Steeep: Support & training for an Escellent Energy Efficiency Performance
The Global Energy Consuption is Growing
The Cost of Energy is Increasing
Climate
Change
High Energy dependence from abroad
01
02
03
04

## Slide 5
Consequences of energy consumption
Energy Efficiency
The consumption of fossil fuels poses major problems: depletion of reserves, energy dependence, supply difficulties and pollution.
The main environmental problem of the current energy consumption worldwide is the greenhouse effect.
The use of private vehicles, heating and even our electricity consumption are responsible for the emission of CO2 into the atmosphere. Each household is responsible for producing up to 5 tons of CO2 per year.
Renewable energies are not exhausted when we consume them because they are renewed naturally. They also have a very reduced environmental impact.
Families, with their behavioral patterns, are decisive to ensure that energy resources are used efficiently.

## Slide 6
Energy Policy of the EU
Energy Efficiency
The Energy Union is a reality and the EU has set course to become a climate neutral economy, whilst maintaining its global competitiveness and creating growth and jobs.
The European Union's energy policy (April 2019) will aim to:
Energy Security
Enhanced resilience of the European energy system by preventing and managing gas crises
The internal energy market
Making the grid fit for an increased share of renewable energy
Putting the consumer at the heart of the energy market
Market coupling - reduced and more equal energy costs for consumers throughout Europe

## Slide 7
Energy Efficiency
Energy Efficiency
Energy Policy of the EU
New energy efficiency target of at least 32.5% by 2030
New energy performance of buildings rules aiming at decarbonisation of building stock by 2050
Clearer and simpler energy efficiency labelling rules help households save almost €500 per year
Between 2014 to 2020, €18 billion from the European structural investment fund are allocate to energy efficiency
There are 900.000 jobs in the energy efficiency sector in Europe today •
€2.5 billion Horizon 2020 funding for the period 2018-2020 to decarbonise the EU’s building stock
Decarbonisation
The EU was instrumental in brokering the Paris Agreement and making it operational
The EU has put in place a comprehensive legislative framework to achieve at least 40% emission reduction by 2030
New renewable energy target of at least 32% by 2030
4 million ‘green jobs’ in the EU today, 1.4 million jobs in the renewable energy sector
Decarbonisation strategy “clean planet for all” for a climate neutral Europe in 2050
17.5% of final energy consumption in Europe came from renewable energy in 2017

## Slide 8
Energy Management has to do with the systematic use of management tools and technology to improve the energy performance of an organization. To be fully effective, it needs to be integrated, proactive and should encompass energy purchases, energy efficiency and renewable energies.
Carbon Trust Energy Management Guide
Energy Management
“
”

## Slide 9
TRANSPORT
CONSTRUCTION
INDUSTRIES
Change of mobility
Urban planning
Infrastructure
Changing prices
Heating and air conditioner systems
Thermal insulation
Smart technology systems
Zero energy building
Industrial refrigeration
Steam
Compressed Air
Pump system
Energy Efficiency in different fields
AGRICULTURE
Fuels
Irrigation
Building insulation
Lighting

## Slide 10
Source: “Guía Práctica de la Energía. Consumo Eficiente y Responsable”. IDAE Instituto para la Diversificación y Ahorro de la Energía
Energy, consumption and energy supply
Every time we consume more energy: at the current rate it will only take 35 years to double the world energy consumption and less than 55 years to triple it.
The sectors of housing and transport have been those that have increased their consumption in recent years.
Europe has an average external energy dependence of 50%.
The main source of energy for energy consumption is oil and its derivatives (gasoline, diesel, butane and propane).
Renewable energies are not exhausted when we consume them, since they are renewed, naturally. In addition, they have a practically zero environmental impact.

## Slide 11
Why do you need a company to make an effective use of energy?
Energy Management
Effective
Energy
The cost of energy can be managed
Corporate responsibility.
Social pressure.
Regulatory control and establishment of limits (energy regulation, CO2 emissions, ...).
Can be a customer requirement.
To increase market value mercad.

## Slide 12
Benefits for your company
Energy management
Cost savings and improvement of competitiveness.
More information in your company.
  Strategic planning and opportunity for improvement.
Risk reduction
Motivation for employees
Image

## Slide 13
Energy efficiency in industrial energetic uses:
The energy consumption and associated costs are related to technical and human factors.
To analyze the use of energy in your company, it is necessary to consider the following points:
Lighting system
Electric drives
Compressed air systems
Pumping
Industrial refrigeration
Process heating
Steam production
Office equipment

## Slide 14
Lighting system

## Slide 15
Maximize the use of natural light.
Reduce artificial lighting to minimum levels.
Turn off the switch
Turn off the lights if they are not needed and in areas that are not occupied.
Divide the lighting so that there are different switches is to control different sections.
Natural light
Choose light colors for the interior walls of the building.
The darker the colors, the more artificial light will be needed.
Investments:
Install timers and / or presence sensors (10% to 20% savings) in services, corridors, basements, garages ...
Install drivers for the use of daylight in each area that receives natural light.
Replace the electromagnetic coils of fluorescent tubes with more efficient electronic ballasts.
Switch to efficient lighting.
Light colors
Energy efficiency in industrial energetic uses:
Together, these investments can reduce energy consumption and costs up to 45%.

## Slide 16
Energy efficiency in industrial energetic uses:

## Slide 17
Take an inventory of the installed electric motors with the following methodology:
Identify the engines and the associated process (pumping, ventilation, drives…);
Identify the electrical characteristics: power, demand current, voltage, power factor, operation regime;
Knowledge of the number of hours the engine operates;
Load or demand factor;
Maintenance program;
Consumption as possible (meter or grid analyzer for measurement).
Electric drives
Correct selection of the engines
It is very common to see oversized engines, which makes the nominal power too high compared to what is needed to cover the needs
Take an inventory
Replace old engines
Replace old engines with new ones with high efficiency.
VFD:
Install Variable Frequency Drive.
The objective is to modify the engine speed to ensure that it is always operating in optimal conditions.

## Slide 18
Compressed Air

## Slide 19
Install more dryers performing.
Check regularly the pressure drops of the driers.
Respect the periodicities of maintenance.
If necessary, call in a refrigeration specialist qualified for the maintenance of the cold circuit.
Compressed Air
Dryer
Avoid regulations by throttling of the suction air
Avoid the no-loads of air compressor.
Install an electronic variation speed to adapt production to the real need of compressed air.
Install a management system and regulation of compressors cascade according to the need of air
Regulation
Close the not used network’s parts.
Heat Recovery
Closing the network to limit the gaps pressure at the end of the network
Compressed Air Network
Look for and seal leaks regular (at least once a year).
The leaks are responsible for a significant waste, frequently around 40 to 50% of the overall consumption.
Filters
Replace tools if possible pneumatic power tools. The price of the pneumatic kWh is 20 times higher than the price of the electric kWh.
Pneumatic Tools

## Slide 20
Pumping
Replace or modify pumps oversized.
Choose the pump according to the needs of the system
Apply a coating that reduces friction inside the wheel and the volute centrifugal pumps
Restore internal tolerances shoes
Identify the pumps in cavitation
Pumps
Put in place a monitoring system for the entire network.
Process
Recover the rejected heat by the compressor for space heating or water production hot.
About 80% of electric power compressor is transformed into heat.
Valves
Valves
Install electronic speed variation when it allows to increase the energy efficiency of the pumping system.
Stop the pumps when they do not need to be Operating. Do not pump for nothing.

## Slide 21
Industrial Refrigeration

## Slide 22
Speed variation
For low temperatures, use two-stage cycles or cycles to economizer.
Install power compressors judiciously tiered to cover better the whole range of powers called.
Compressors
Install speed variation on at least one of the compressors
For screw compressors, privilege the regulation of power by speed variation rather than by drawer.
Install a cold buffer storage if necessary. It is also possible to size the decoupling bottle so that she can eventually play a storage role.
Storage
Install a recovery system heat on the cold group
For screw compressors: recover the heat on the oil circuit.
Up to 25% rejected heat can be valorized at a temperature of 50 - 60 ° C.
Heat recovery
Distribution
Check the state of the cold circuit insulation and repair if necessary.
Adopt a strategy adequate and powerful of defrosting
Insulation & Defrost
Regulate the flow of refrigerant fluid by electronic speed variation on the secondary distribution pump.
Regulate the coolant flow on the primary circuit versus flow on the secondary circuit.
Prefer large sized evaporators to reduce pinching.
10% more surface is 1°C won, so 2 to 3% of the energy consumed.
Evaporator
Lighting is a contribution of heat
Set up efficient lighting systems in the cold rooms
Lightning
Set up protection's effective openings (curtains with straps, air curtains, quick-open doors).
Set up buffer locks and decrease openings / closures of the area.
Inlets can be responsible for 20 to 40% of the balance sheet refrigeration system.
Cold room openings
Industrial Refrigeration

## Slide 23
hhot water
Cool water
gases output
fuel input
burner
Gas circuit
Process heating

## Slide 24
1 ° C temperature increases = The energy saving approximately 6%
Process heating
Adjust the temperature of rooms and boilers
Measures without cost
Thermal insulation in boilers, hot water tanks and water pipes.
Thermal isolation
1 mm of soot = 50 ° C smoke temperature = loss of performance of 4% -8%
Clean the boiler
Place a temperature control on the heating system.
Choose hot air instead of hot air systems
Recover the heat from the ventilation and reuse it.
Reduce the zones to heat.
Other measures
Large consumers of electricity and thermal energy should consider cogeneration.
It is advisable to use solar collectors to heat the water
Condensing boiler: designed to utilize the latent heat released by the condensation of the water vapor.
About 109% efficiency
Up to 40% savings compared to conventional boilers
High efficiency boilers

## Slide 25
Thermodynamic
With float
Steam production

## Slide 26
Steam production
Install a recovery system heat lost during purges, you can save between 1 and 4% of energy.
Heat Recovery
Repair leaks regularly. A single leak of 3.18 mm diameter on a steam network at 7 bar causes a loss of € 3,900 / year.
Driving with insulation wet gives way 30 times more only when it is dry.
Steam Network
Install an economizer to preheat the water supply of a steam boiler.
Energy savings of 2 to 5% are possible.
Economizer
Check the traps regularly.
In installations where the traps are not frequently checked, 30% of them can be defective and run away.
Regular monitoring can lower this rate to 5%.
Steam Trap
A supply of water not insulated can lose up to 70% of its thermal energy.
Supply of Water
Economizer
If possible, reduce the pressure of the network. If there are regulators at the entrance of all consumers, a network high pressure is not necessary.

## Slide 27
Office equipment

## Slide 28
The most important consumption of the office.
Computers and monitors with the "ENERGY STAR" condition hibernate automatically when they are not used and almost all vendors sell them.
Both computers and monitors in hibernation consume approximately 15% of their maximum power of use.
Photocopiers and printers
"ENERGY STAR" photocopiers can reduce the annual electric cost of photocopiers by up to 60%.
Photocopiers that allow double-sided or duplex copies help save energy and reduce the cost of paper.
Computers
FAX
The fax needs to be available 24 hours a day, therefore, it has a great potential to save energy.
It can hibernate up to 15 to 45 watts or less when not in use, and can save approximately 50% in its annual energy cost.
Turn off the computer when it is not in use (at night or on weekends). There are timers that turn off the equipment at certain times of the day.
If the computer has to be on during the night or during weekends, save money by turning off the monitor.
The energy saving features have to be established by the user in many products. Check the configuration periodically or each time you install new equipment to ensure that the power saving mode is on.
Screen protectors do not save energy. Its purpose is to extend the useful life of the screen.
Laser printers consume more energy than inkjet printers. Color printers use more energy than those that only print in black and white.
Laptops consume much less than a PC.
Other tips
Office equipment

## Slide 29
Thanks For Your Attention!
This project has received funding from the European Union’s H2020 Coordination Support Action under Grant Agreement No.785047.

## Slide 30
Towards a sustainable agro-food industry. Capacity building programmes in energy efficiency.