## Slide 1
Energy efficiency:
Introduction of the Energy efficiency in the company
This project has received funding from the European Union’s H2020 Coordination Support Action under Grant Agreement No.785047.
Towards a Sustainable Agro-Food Industry. Capacity Building Programmes in Energy Efficiency.

## Slide 2
Why do you need a company to make an effective use of energy?
Energy management
Effective
Energy
The cost of energy can be managed
Corporate responsibility.
Social pressure.
Regulatory control and establishment of limits (energy regulation, CO2 emissions, ...).
Can be a customer requirement.
To increase market value mercad.

## Slide 3
Benefits for your company
Energy management
Cost savings and improvement of competitiveness.
More information in your company.
  Strategic planning and opportunity for improvement.
Risk reduction
Motivation for employees
Image

## Slide 4
Energy efficiency in industrial energetic uses:
The energy consumption and associated costs are related to technical and human factors.
To analyze the use of energy in your company, it is necessary to consider the following points:
Lighting system
Electric drives
Compressed air systems
Pumping
Industrial refrigeration
Process heating
Steam production
Office equipment

## Slide 5
Lighting system

## Slide 6
Maximize the use of natural light.
Reduce artificial lighting to minimum levels.
Turn off the switch
Turn off the lights if they are not needed and in areas that are not occupied.
Divide the lighting so that there are different switches is to control different sections.
Natural light
Choose light colors for the interior walls of the building.
The darker the colors, the more artificial light will be needed.
Investments:
Install timers and / or presence sensors (10% to 20% savings) in services, corridors, basements, garages ...
Install drivers for the use of daylight in each area that receives natural light.
Replace the electromagnetic coils of fluorescent tubes with more efficient electronic ballasts.
Switch to efficient lighting.
Light colors
Energy efficiency in industrial energetic uses:
Together, these investments can reduce energy consumption and costs up to 45%.

## Slide 7
Energy efficiency in industrial energetic uses:

## Slide 8
Take an inventory of the installed electric motors with the following methodology:
Identify the engines and the associated process (pumping, ventilation, drives…);
Identify the electrical characteristics: power, demand current, voltage, power factor, operation regime;
Knowledge of the number of hours the engine operates;
Load or demand factor;
Maintenance program;
Consumption as possible (meter or grid analyzer for measurement).
Electric drives
Correct selection of the engines
It is very common to see oversized engines, which makes the nominal power too high compared to what is needed to cover the needs
Take an inventory
Replace old engines
Replace old engines with new ones with high efficiency.
VFD:
Install Variable Frequency Drive.
The objective is to modify the engine speed to ensure that it is always operating in optimal conditions.

## Slide 9
Compressed Air

## Slide 10
Install more dryers performing.
Check regularly the pressure drops of the driers.
Respect the periodicities of maintenance.
If necessary, call in a refrigeration specialist qualified for the maintenance of the cold circuit.
Compressed Air
Dryer
Avoid regulations by throttling of the suction air
Avoid the no-loads of air compressor.
Install an electronic variation speed to adapt production to the real need of compressed air.
Install a management system and regulation of compressors cascade according to the need of air
Regulation
Close the not used network’s parts.
Heat Recovery
Closing the network to limit the gaps pressure at the end of the network
Compressed Air Network
Look for and seal leaks regular (at least once a year).
The leaks are responsible for a significant waste, frequently around 40 to 50% of the overall consumption.
Filters
Replace tools if possible pneumatic power tools. The price of the pneumatic kWh is 20 times higher than the price of the electric kWh.
Pneumatic Tools

## Slide 11
Pumping
Replace or modify pumps oversized.
Choose the pump according to the needs of the system
Apply a coating that reduces friction inside the wheel and the volute centrifugal pumps
Restore internal tolerances shoes
Identify the pumps in cavitation
Pumps
Put in place a monitoring system for the entire network.
Process
Recover the rejected heat by the compressor for space heating or water production hot.
About 80% of electric power compressor is transformed into heat.
Valves
Valves
Install electronic speed variation when it allows to increase the energy efficiency of the pumping system.
Stop the pumps when they do not need to be Operating. Do not pump for nothing.

## Slide 12
Industrial Refrigeration

## Slide 13
Speed variation
For low temperatures, use two-stage cycles or cycles to economizer.
Install power compressors judiciously tiered to cover better the whole range of powers called.
Compressors
Install speed variation on at least one of the compressors
For screw compressors, privilege the regulation of power by speed variation rather than by drawer.
Install a cold buffer storage if necessary. It is also possible to size the decoupling bottle so that she can eventually play a storage role.
Storage
Install a recovery system heat on the cold group
For screw compressors: recover the heat on the oil circuit.
Up to 25% rejected heat can be valorized at a temperature of 50 - 60 ° C.
Heat recovery
Distribution
Check the state of the cold circuit insulation and repair if necessary.
Adopt a strategy adequate and powerful of defrosting
Insulation & Defrost
Regulate the flow of refrigerant fluid by electronic speed variation on the secondary distribution pump.
Regulate the coolant flow on the primary circuit versus flow on the secondary circuit.
Prefer large sized evaporators to reduce pinching.
10% more surface is 1°C won, so 2 to 3% of the energy consumed.
Evaporator
Lighting is a contribution of heat
Set up efficient lighting systems in the cold rooms
Lightning
Set up protection's effective openings (curtains with straps, air curtains, quick-open doors).
Set up buffer locks and decrease openings / closures of the area.
Inlets can be responsible for 20 to 40% of the balance sheet refrigeration system.
Cold room openings
Industrial Refrigeration

## Slide 14
hhot water
Cool water
gases output
fuel input
burner
Gas circuit
Process heating

## Slide 15
1 ° C temperature increases = The energy saving approximately 6%
Process heating
Adjust the temperature of rooms and boilers
Measures without cost
Thermal insulation in boilers, hot water tanks and water pipes.
Thermal isolation
1 mm of soot = 50 ° C smoke temperature = loss of performance of 4% -8%
Clean the boiler
Place a temperature control on the heating system.
Choose hot air instead of hot air systems
Recover the heat from the ventilation and reuse it.
Reduce the zones to heat.
Other measures
Large consumers of electricity and thermal energy should consider cogeneration.
It is advisable to use solar collectors to heat the water
Condensing boiler: designed to utilize the latent heat released by the condensation of the water vapor.
About 109% efficiency
Up to 40% savings compared to conventional boilers
High efficiency boilers

## Slide 16
Thermodynamic
With float
Steam production

## Slide 17
Steam production
Install a recovery system heat lost during purges, you can save between 1 and 4% of energy.
Heat Recovery
Repair leaks regularly. A single leak of 3.18 mm diameter on a steam network at 7 bar causes a loss of € 3,900 / year.
Driving with insulation wet gives way 30 times more only when it is dry.
Steam Network
Install an economizer to preheat the water supply of a steam boiler.
Energy savings of 2 to 5% are possible.
Economizer
Check the traps regularly.
In installations where the traps are not frequently checked, 30% of them can be defective and run away.
Regular monitoring can lower this rate to 5%.
Steam Trap
A supply of water not insulated can lose up to 70% of its thermal energy.
Supply of Water
Economizer
If possible, reduce the pressure of the network. If there are regulators at the entrance of all consumers, a network high pressure is not necessary.

## Slide 18
Office equipment

## Slide 19
The most important consumption of the office.
Computers and monitors with the "ENERGY STAR" condition hibernate automatically when they are not used and almost all vendors sell them.
Both computers and monitors in hibernation consume approximately 15% of their maximum power of use.
Photocopiers and printers
"ENERGY STAR" photocopiers can reduce the annual electric cost of photocopiers by up to 60%.
Photocopiers that allow double-sided or duplex copies help save energy and reduce the cost of paper.
Computers
FAX
The fax needs to be available 24 hours a day, therefore, it has a great potential to save energy.
It can hibernate up to 15 to 45 watts or less when not in use, and can save approximately 50% in its annual energy cost.
Turn off the computer when it is not in use (at night or on weekends). There are timers that turn off the equipment at certain times of the day.
If the computer has to be on during the night or during weekends, save money by turning off the monitor.
The energy saving features have to be established by the user in many products. Check the configuration periodically or each time you install new equipment to ensure that the power saving mode is on.
Screen protectors do not save energy. Its purpose is to extend the useful life of the screen.
Laser printers consume more energy than inkjet printers. Color printers use more energy than those that only print in black and white.
Laptops consume much less than a PC.
Other tips
Office equipment

## Slide 20
Thanks For Your Attention!
This project has received funding from the European Union’s H2020 Coordination Support Action under Grant Agreement No.785047.

## Slide 21
Towards a sustainable agro-food industry. Capacity building programmes in energy efficiency.