## Slide 1
Workshop
Best Practice achieved by Monitoring and Benchmarking
This project has received funding from the European Union’s H2020 Coordination Support Action under Grant Agreement No.785047.
Towards a Sustainable Agro-Food Industry. Capacity Building Programmes in Energy Efficiency.

## Slide 2
Best-Practice Examples: How the Food Industry can profit from proper Monitoring and Benchmarking on behalf of baseline models

## Slide 3
Training Unit developed by ÖKOTEC
System Boundaries | Best Practice
Dryers | Process Optimisation from Benchmarking; Energy Efficiency Surveilance; Impacts of Energetic Optimisation
Packaging | Quantification of Energy Efficiency advantage of two alternative packaging lines (Benchmarking); Efficiency Surveilance
Combined Heat and Power Plant | Energy Efficiency Surveilance; Identification of optimisation possibilities regarding Maintenance
Air Compressing Station | Identification of optimisation possibilities regarding operations
Heat Recovery at Air Compression | Energy Efficiency Surveilance in Heat Recovery, Evaluation of Impacts of Optimisation
Best Practice Examples from Monitoring and Benchmarking

## Slide 4
The Effects of the measure can be quantified and investment decisions regarding transfer to the other dryers can be made.
Optimisation of drying process in the second drying phase
Reduction of Tempe- ratures in Heating phase
Energy Cost Reduction
Source of Diagram: ÖKOTEC EnEffCo
Exact Evaluation of Energy Cost savings of a dryer optimisation

## Slide 5
There are 8 different dryers in the company. Having developed Baselines for eachdryer, it can be simulated what one dryer would consume if it would have performed the production task of another dryer
The diagram shows the energy cost advantage of the most efficient dryer in comparison the the dryer, which was actually used to perform the drying task.
Comparing of all the 8 dryers, an energy efficiency ranking can be realised. On basis of that, a process optimisations can be performed (primary usage of the most efficient dryers)
Actual Energy Costs
Bench-mark
Savings potential
Source of Diagram: ÖKOTEC EnEffCo
Benchmarking of dryers

## Slide 6
Training Unit developed by ÖKOTEC
System Boundaries | Best Practice
Dryers | Process Optimisation from Benchmarking; Energy Efficiency Surveilance; Impacts of Burner-Optimisation
Packaging | Quantification of Energy Efficiency advantage of two alternative packaging lines (Benchmarking); Efficiency Surveilance
Combined Heat and Power Plant | Energy Efficiency Surveilance; Identification of optimisation possibilities regarding Maintenance
Air Compressing Station | Identification of optimisation possibilities regarding operations
Heat Recovery at Air Compression | Energy Efficiency Surveilance in Heat Recovery, Evaluation of Impacts of Optimisation
Best Practice Examples from Monitoring and Benchmarking

## Slide 7
The diagram shows the Surveilance of Energy Costs of a drying line on a daily basis by comparing the baseline to actual energy cost values.
In August, there was an unexpected peak in Energy costs and the Energy Manager received an early warning E-Mail by the Energy Surveilance system.
He could react at once and noticed, that the controls were wrongly set during maintenance. He could intervene and avoid high Energy costs, that would have occured if the mistake would not have been noticed.
Unexpected high consumption
Tolerance area (depending on model quality)
Source of Diagram: ÖKOTEC EnEffCo
Energy Surveilance of a Packaging line

## Slide 8
The company went further. It has a second packaging line performing the same task, but applying a different technology. Having baselines for each of the packaging lines, a comparison is possible by benchmarking.
The benchmarking results shows, that one of the packaging lines works much more efficient than the other. For each day the savings potential can be evaluated, if not the less efficient packing line, but the efficient packaging line would have ferformed the packaging task.
On behalf of that, better capacity planning ist possible. Further, a solid investment decision can be made regarding the replacement of the less efficient packaging line
Savings potential
Source of Diagram: ÖKOTEC EnEffCo
Benchmarking of Packaging lines

## Slide 9
Training Unit developed by ÖKOTEC
System Boundaries | Best Practice
Dryers | Process Optimisation from Benchmarking; Energy Efficiency Surveilance; Impacts of Burner-Optimisation
Packaging | Quantification of Energy Efficiency advantage of two alternative packaging lines (Benchmarking); Efficiency Surveilance
Combined Heat and Power Plant | Energy Efficiency Surveilance; Identification of optimisation possibilities regarding Maintenance
Air Compressing Station | Identification of optimisation possibilities regarding operations
Heat Recovery at Air Compression | Energy Efficiency Surveilance in Heat Recovery, Evaluation of Impacts of Optimisation
Best Practice Examples from Monitoring and Benchmarking

## Slide 10
A company has a large CHP which it maintains on a regular basis. During monitoring it was identified, that sometimes the Energy Costs increase already longer times before planned maintenance. In other cases, energetic maintenance was carried out before actually Energy Costs increased.
Source of Diagram: ÖKOTEC EnEffCo
Predictive Maintenance of a Combined Heat and Power plant

## Slide 11
Source of Diagram: ÖKOTEC EnEffCo
Predictive Maintenance of a Combined Heat and Power plant
Now an early warning system is in place informing the Energy Manager about energy costs increase, so he can perform maintenance when it is actually needed.

## Slide 12
Training Unit developed by ÖKOTEC
System Boundaries | Best Practice
Dryers | Process Optimisation from Benchmarking; Energy Efficiency Surveilance; Impacts of Burner-Optimisation
Packaging | Quantification of Energy Efficiency advantage of two alternative packaging lines (Benchmarking); Efficiency Surveilance
Combined Heat and Power Plant | Energy Efficiency Surveilance; Identification of optimisation possibilities regarding Maintenance
Air Compressing Station | Identification of optimisation possibilities regarding operations
Heat Recovery at Air Compression | Energy Efficiency Surveilance in Heat Recovery, Evaluation of Impacts of Optimisation
Best Practice Examples from Monitoring and Benchmarking

## Slide 13
On behalf of monitoring, a company noticed that on weekends the energy costs of an air compression station were higher than expected. This regarded phases were low amounts of compressed air were produced after times of high production.
After analyses it became clear, that optimisation in controls could avoid this bevior. Nowing the saving potentials of Energy Costs, the company could perform an investment evaluation of additional controls.
Source of Diagram: ÖKOTEC EnEffCo
Monitoring of a large air compressing station

## Slide 14
Training Unit developed by ÖKOTEC
System Boundaries | Best Practice
Dryers | Process Optimisation from Benchmarking; Energy Efficiency Surveilance; Impacts of Burner-Optimisation
Packaging | Quantification of Energy Efficiency advantage of two alternative packaging lines (Benchmarking); Efficiency Surveilance
Combined Heat and Power Plant | Energy Efficiency Surveilance; Identification of optimisation possibilities regarding Maintenance
Air Compressing Station | Identification of optimisation possibilities regarding operations
Heat Recovery at Air Compression | Energy Efficiency Surveilance in Heat Recovery, Evaluation of Impacts of Optimisation
Best Practice Examples from Monitoring and Benchmarking

## Slide 15
kW heat recovery
During Monitoring of the heat recovery of an air compressor station, a company identified possibilities to enhance heat regeneration
White Line: Heat thas would have been expected to be recoverd according under actual conditions (Baseline)
Dark Grey Line: Heat that was actually recovered
Light Green: Tolerance area, depending on quality of the baseline model
Source of Diagram: ÖKOTEC EnEffCo
Evaluation of better heat recoverage from an air compressor

## Slide 16
After Realisation, the effects could be evaluated. Now, knowing the effects of the measure, the company can transfer it other air compression units.
kW heat recovery
Dark Green: Securly evaluated gain in heat recoverage
Source of Diagram: ÖKOTEC EnEffCo
Evaluation of better heat recoverage from an air compressor

## Slide 17
Towards a sustainable agro-food industry. Capacity building programmes in energy efficiency.